## Slide 1
Cognitive Multi-Robot Search and Rescue
Through Collaborative Perception and Reasoning
DA2 implementation review
Name | Registration No.
Aadavan Elavalagan | 23BRS1268
K S Vinoth | 23BRS1209
Shyam Sundar | 23BRS1192
Madhavan A Ramanujan | 23BRS1227
System: 3-robot simulation in ROS 2 Jazzy + Gazebo Harmonic
Allocation: MAPPO (learned) compared against a rule-based baseline
Notes: Open with one line: in DA1 we proposed this system, and today we are showing the working implementation and the first benchmark data.

## Slide 2
Problem and approach
Why a single robot is not enough
After a disaster, rescuers have limited visibility and face personal risk, so every minute matters.
A single robot sweeping a large collapsed structure is far too slow to find victims in time.
Just merging occupancy maps is not enough: robots still need to decide where to search next without duplicating each other's work.
What we proposed in DA1 (and built since)
Robots build one shared map together (collaborative SLAM).
Victim and hazard detections from any robot are stored in a common semantic map, so the whole team knows what has been found.
A multi-agent reinforcement learning policy (MAPPO) learns how to divide the search area between robots. We compare it against a simple rule-based allocator.
The difference between our system and plain map merging: the shared map also carries meaning (victims found, regions already searched), and the allocator uses that meaning to decide where each robot should go next.
Notes: The last line on this slide is the 'cognitive' claim from our abstract in one sentence: shared semantic state feeding the allocation decision, not just occupancy fusion.

## Slide 3
System architecture
Every block below is an implemented ROS 2 node in the repository.
Each robot (x3)
slam_toolbox
local map per robot (namespaced)
detector (YOLO or HSV)
camera + lidar range = victim position
Nav2 + Smac (A*)
navigates to assigned regions
Shared state
map_merge
fuses N local maps into one
sar_memory
shared semantic map (victims, hazards)
frontier
splits map into 16 search regions
Decision layer
MAPPO allocator
learned region assignment
rule allocator
greedy nearest-frontier baseline
sar_eval
coverage, victims, overlap, timings
Data flow: each robot publishes /robot_i/map and /detections; the shared layer publishes /map_merged, /semantic_map and /regions to the allocators.
The two allocators are interchangeable: both publish /robot_i/goal, which Nav2 follows, and sar_eval logs /mission_metrics for the benchmark.
Message and topic definitions are written down in docs/interfaces.md; they were fixed early so the four of us could build in parallel.
Notes: Walk left to right. The swap between MAPPO and the rule allocator is the whole benchmark design: same interface, two brains.

## Slide 4
Status of the five objectives from the abstract
Objective | What it means in the system | Status | Evidence
O1 Collaborative SLAM | Fused global map from 3 robots | Done | sar_slam map fusion + tests
O2 Semantic understanding | Victim/hazard detection in map frame | Done | sar_perception detector node
O3 Shared memory | One semantic map every robot can query | Done | sar_memory node + RViz view
O4 RL task allocation | MAPPO assigns search regions | Trained, ~148k steps | training/runs/mappo_v1
O5 Benchmark vs baseline | Learned vs rule-based allocator | First results | benchmark_summary.json
O4 and O5 are functional end to end; what remains before the final review is the Gazebo-level benchmark matrix and a longer training run.
Notes: Be straight about O4/O5: built and running, but the learned policy has not yet beaten the greedy baseline. More training is scheduled and needs no redesign - slide 9 covers this.

## Slide 5
What has been built so far
11
ROS 2 packages
43
Python modules
9
unit tests passing
341
training episodes logged
Training code (pure Python)
sar_gym: grid search environment, 16 region actions, A* executor
mappo: shared actor + centralized critic, GAE, PPO-clip
train.py / evaluate.py: training and benchmark scripts
Robot code (ROS 2 Jazzy)
sar_worlds + sar_robot: maze world and diff-drive robot
sar_slam, sar_memory, sar_nav: fusion, semantic map, frontiers
sar_alloc_rule and sar_alloc_rl: the two allocators
Tests and docs
Contract tests: training vs deployment observation spec
Map fusion unit tests (rotation, offsets, unknown cells)
BUILD_PLAN.md, README, docs/interfaces.md
The whole system starts with one command: ros2 launch sar_bringup multi_sar.launch.py robots:=3 allocator:=rule
Counts from a repository audit on 2026-09-12. Environment: WSL2 (Ubuntu 24.04), ROS 2 Jazzy LTS, Gazebo Harmonic.
Notes: Message: this was engineered like a team project, not a notebook. Interfaces were fixed first; contract tests keep training and deployment from drifting apart.

## Slide 6
How the allocation policy is trained
1. Shared maze generator
The same code generates the training maps and the Gazebo world, so the policy practises on the room layouts it will actually face.
2. Lightweight grid environment
Training runs on a 64x64 grid: each robot picks one of 16 regions, an A* executor drives it there. No physics simulation needed for allocation decisions.
3. MAPPO (centralized training)
One critic sees the full map during training; each robot's actor only sees its own view at execution time (CTDE).
4. Deployment
The trained checkpoint is loaded by the sar_alloc_rl ROS node, which publishes region goals. A unit test pins the observation format.
Reward function:
r = +0.10 (new area explored) + 10 (victim located) - 0.02 (cell another robot already searched) - 0.01 (time) - 0.05 (choosing a finished region)
This is why training takes minutes on a CPU instead of days in the simulator.
Notes: Expected question: why not train directly in Gazebo? Answer: allocation is a slow, region-level decision; the grid abstraction trains in seconds per episode, and the observation contract (unit-tested) carries the policy into the simulator unchanged.

## Slide 7
Training results
Chart: training episode (logged every 10)
| 10 | 60 | 110 | 160 | 210 | 260 | 310 | 340
Episodic reward | 77.4 | 77.1 | 71.9 | 69.1 | 70.1 | 77.1 | 75.7 | 73.8 | 65.2 | 60.6 | 55.4 | 59.7 | 69.1 | 67.2 | 62.9 | 57.2 | 60 | 61.3 | 66.2 | 65 | 62.7 | 55.9 | 53 | 59.3 | 61.3 | 61.4 | 64.6 | 61.5 | 60.6 | 55.5 | 60.6 | 70 | 69.4 | 65.7
What the curve shows
Map coverage settled at 83-86% early in training and stayed there.
Reward plateaus around 66-74: the basic behaviour (spread out, do not re-search, pick up victims) is learned within the first third.
The remaining steps did not yet convert into beating the rule baseline - see next slide.
Data: training/runs/mappo_v1, 34 checkpoints over ~148k environment steps (MAPPO, 3 agents, GAE 0.95, lr 3e-4).
Notes: Read it honestly: the learning happened early and then plateaued. That is why the benchmark is at parity, not dominance, and why a longer run is the next step.

## Slide 8
Benchmark: learned policy vs baselines
Victims located (of 5), higher is better
Chart: 
| Rule-based | MAPPO | Random
Victims located (of 5), higher is better | 4.25 | 3.25 | 3.75
Rule-based finds 1 victim more on average.
Mission steps until finished, lower is better
Chart: 
| Rule-based | MAPPO | Random
Mission steps until finished, lower is better | 138 | 444 | 425
Rule-based finishes most missions early; MAPPO often runs to the step cap.
Map coverage: 85-86% for all three policies (no significant difference). Time to first detection: MAPPO 43 steps, rule-based 49, random 57.
Summary: greedy frontier allocation is a strong baseline and the learned policy has not beaten it yet at ~150k training steps. Where the learned policy already looks better is detection speed; victims and mission time need more training.
Data: training/evaluate.py, 4 held-out maps x 2 episodes, 3 robots, 600-step cap. Full table: reports/benchmark_summary.json.
Notes: Do not hide the negative result. If asked why greedy wins: pure frontier coverage is close to greedy-optimal; our hypothesis is that learned use of semantics (victim priors) pays off with more training and in the full simulator.

## Slide 9
What works, what does not yet, and what we do next
Working
Full pipeline runs end to end: detection, shared semantic map, allocation, navigation, metrics.
Multi-robot map fusion is unit-tested (rotation, offsets, unknown areas).
Training and deployment share a fixed observation contract, enforced by tests.
The learned policy already reaches the same map coverage as the hand-written allocator.
Not there yet -> our plan
Victims found per mission still trails the greedy baseline. Plan: 300-500k more training steps on a Colab GPU (2-3 hours) and a reward-weight tune.
Deterministic (argmax) policy gets stuck at this training level. Plan: keep sampling at deployment (already the default), re-test after longer training.
Benchmarks so far are in the abstract environment. Plan: run the Gazebo-level experiment matrix (10 runs per allocator), then the report.
All three gaps were written down with their fixes in the build plan (BUILD_PLAN.md, section 7) before implementation started. None of them requires a redesign.
Notes: This is the credibility slide. A pre-registered risk register with honest status reads as maturity. If asked about MAPPO sample efficiency: we used the Yu et al. 2021 hyperparameters and the action space is already minimal (16 regions).

## Slide 10
Plan until the final review
When | Milestone | What happens
Weeks 1-2 | Simulator bringup | Install WSL2 + ROS 2 Jazzy + Gazebo, run and record the 3-robot mission (rule-based) as the demo backup.
Weeks 2-3 | Gazebo benchmark | 10 runs per allocator with scripts/run_experiments.sh; produce coverage, victims and overlap curves.
Weeks 3-4 | Longer training | 300-500k steps on Colab GPU, re-benchmark, freeze the final checkpoint.
Weeks 5-6 | Report | Optional ablation (allocation without semantic memory) and the final report with the recorded demo.
The recorded mission video is the fallback for the live demo; the rule-based allocator is the default demo, RL on request.
Notes: Weeks are counted from this review. Critical path is the bringup; everything after that is repeatable scripts. Pre-agreed scope cuts if time runs short: D* Lite, YOLO fine-tuning, 4th robot.

## Slide 11
Summary
All five objectives from the DA1 abstract are implemented and running.
The learned allocator matches the rule-based baseline on coverage today; closing the remaining gap is a training-budget problem, not a design problem.
Next: Gazebo-level benchmark matrix, longer training, final report and recorded demo.
Thank you. Questions?
Repository: cognitive-sar/ (BUILD_PLAN.md, docs/interfaces.md, reports/)
Demo command: ros2 launch sar_bringup multi_sar.launch.py robots:=3 allocator:=rule
Aadavan Elavalagan (23BRS1268), K S Vinoth (23BRS1209), Shyam Sundar (23BRS1192), Madhavan A Ramanujan (23BRS1227)
Notes: Offer the live demo here. Keep the terminal open with the repo and the metrics CSV ready.